# DUAL TR FAILURE

## WITH NO LOSS OF AC POWER

PILOT INDICATIONS

- SLAT INDICATOR(INTRANSIT

- FLAP INDICATOR(11 O’CLOCK POSITION

- GEAR INDICATORS(INTRANSIT

- HIS,ADI,BDHI(WARNING FLAGS IN VIEW

- NO ANNUNICATOR OR MASTER CAUTION LIGHTS

- AFCS(INOPERATIVE

- NORMAL AND ALTERNATE PITCH TRIM(INOPERATIVE

BUSSES LOST

- MAIN DC #1 AND #2

- AVIONICS DC #1 AND #2

- ISOLATED DC

- AVIONICS ISOLATED DC

FE INDICATIONS(BATTERY LIGHT AND ISO DC OFF

INSTRUMENT POWER SWITCH TO EMERGENCY RESTORE 2 ISOLATED DC BUSES

LOSE NAV AC BUS #1

- AUTOPILOT

- BDHI’S

- INS#3 EXITATION

- TACAN’S

- ADF’S

SYSTEMS AFFECTED

- LANDING GEAR(BUTTON DOWN

- THRUST REVERSERS(INOPERATIVE

- CANNOT DISCONNECT CSD(MUST SHUT DOWN ENGINE TO DO