NAV EQUIPMENT

C-12 AND N-1

NO. 1 COMPASS				NO. 2 COMPASS

PILOT HSI					CP HSI

CP BDHI, RMI					PILOT BDHI RMI

FDMS

MANUAL - (man head) Bank steering bars drive to selected heading bug

NORMAL - Bank steering bars drive to selected nav solution course

SELECTED SYSTEM NAV OFF - lite illuminates when both pilots have selected the

nav aid TAC VOR ILS MLS on the FDMS

STATION PASSAGE

VOR - FIRST POSITIVE TO FROM INDICATION

TAC - AFTER DME STOPS DECREASING

ADF - NEEDLES PASS 90 DEGREE OF INBOUND COURSE

ACCURACY

VOR/TAC  +/- 4

DME +/- 0.5 OR 3%

PITOT STATIC

Altimete, VVI and AS receive pitot/static inputs

Left Pitot tube supplies Pilot gauge, Autopilot, SCNS

Right Pitot tube supplies CP and Nav system

TAS indicator is at Navigator station and SCNS

IAS indicator at P and CP

Barber pole indicates max structural speed at sea level

For unusual Attitudes

Verify

If failed ADI, turn away from needle and center ball

COMMS

P, CP talk on hit mic

P,CP, N can all talk outside the aircraft

P, CP, N , E can listen to outside radio traffic

UHF 1 isolated DC and can be tuned independent of SCNS

Use top antenna for comms on ground, bottom for comms in air & never AUTO

TRANSPONDER

Master switch applies power to the system

Hold holds mode 4 codes if selected 15s prior to power shutdown

RAD TEST MONITOR.  Used by MX to monitor mode 4 ops

TEST Toggle  allows testing of all transponder modes

MODES: 1, 2, 3A, C, 4

Mode 1 and 2 is for GCI/military

Mode 3 ATC

Mode C Altitude encoding off of pilot’s altimeter set at 29.92

Mode 4 is IFF

Antenna select switch should be in both for normal operation

IDENT toggle generates a coded reply on modes 1 and 3

RADAR ALT

Rotate alt set knob to turn on and

Press alt set knob to test

Provides absolute altitude above terrain

Accuracy diminishes over water, ice, and snow

HYDRAULIC

BLEED AIR

ELECTRICAL

BASICS

AC Powers heavy loads

AC power sources: External AC, ATM, Engine generators

AC Engine Generators: 400Hz, 3 phase, 115/200V, 40kVA max load 1.05

AC ATM Generator: 400 Hz, 3 phase, 115/200 V,

20kVA, .66 load, when temp > 104 F

30kVA, 1.00 load when fan on on gnd and temp < 104 F

DC powers valves and controls

DC system Max load - 1.03

DC power sources: External DC, Battery, 4 Transformer Rectifiers

External DC

Cannot charge battery

Battery - 24 volts, Lead Acid, 2 interchangeable batts: INS and reg

21 v minimum for operation

18 v required to close relay

12 v below this amount relay will open

TR’s convert 115v AC to 28v DC

Acceptable range (25 - 30 volts)

ESS AC powers TR 1 & 2  for ESS DC

MAIN AC powers TR 3 & 4 for MAIN DC

In air DC Power travels MAIN -> ESS ONLY

1 Main TR and 1 ESS TR will power all DC in air

Must have at least one ESS TR

Loss of both MAIN DC TR’s in flight will lose MAIN DC BUS

TD Switch allows RCR to let ESS DC power MAIN DC on gnd

K-RELAYS

Determine what powers what

Relays located on station 245

ATM exclusively powers ESS AC

One Gen powers ESS AC & MAIN AC

Two Gen power all four AC BUSSES

Symetrical Generators take care of Symetrical For 2 generators out on one wing

Wing takes care of wing if only one generator is out

AC Busses

ALL PRESSURE GAGES, 26 VOLT AC

FUEL SWITCHES ?

FLAP MOTORS ?

CP INSTRUMENT BUS

Powered by either ESS AC or ISOL DC

No.1 and 2 Flight Director gyros

AC INSTRUMENT and FUEL CONTROL  PANEL

Automatic switch from DC to AC Only

Powered by either ESS AC or ESS DC

Two stepdown transformers to 26V 1phase

TRFMR 1:  (1FEB34) Fuel press, Emer brake Boost press gage, 3 oil press, 4 oil press

Hydraulic Gauges 122 2 122

All others powered by No. 2 TRFMR

LOX, TORQUE, TIT, FUEL FLOW, FUEL QUANTITY,

LEFT HAND - gen 1 engine 1

COMFORT BUSS

NESA

GALLEY

#1 MAIN FUEL TANK PUMP

FORWARD PUMP ON LH EXTERNAL TANK

OVERHEAD FAN IN CARGO

ESSENTIAL - gen 2 engine 2

MAJOR PUMPS AND MOTORS

#2 MAIN FUEL TANK PUMP

SUCTION BOOST PUMPS

FEATHER PUMP MOTORS

NAV INSTRUMENTS

SECONDARY AC POWER

CP’S INSTRUMENT

AC INSTRUMENT AND FUEL

MAIN - gen 3 engine 3

DUMP BUS

ALL MAIN DUMP PUMPS

AFT EXTERNAL PUMPS

#3 MAIN FUEL PUMP

AUX TANK PUMPS

2 TRANSFORMER RECTIFIERS

RADAR

RIGHT HAND - gen 4 engine 4

ANTI-ICE

#4 MAIN BOOST PUMP

PROP ANTI-ICE / DE-ICE

FORWARD PUMP IN RH EXTERNAL TANK

DC Busses

OPENS JETTISON VALVES

CLOSES CROSSFEED VALVES (AUX/EXT)

FUEL QUANTITY

MAIN

LIGHTS

FLAP CONTROL VALVE

ANTI-SKID CONTROL VALVE

ESSENTIAL

AUTO PILOT

SCNS

PILOT PITOT HEAT

AC INSTRUMENT AND FUEL CONTROL

LANDING GEAR SWITCH

ISOLATED

UHF1

CP AND NAV PITOT HEAT

CP INSTRUMENT BUS

NO 1, NO 2, FLIGHT DIRECTOR GYROS, ADI

ATM CONTROLS

GTC CONTROLS AND START

INTERPHONE

BATTERY

FAAJIVEEES

F IRE AGENT

A LARM BELLS

A C POWER SOLENOID

J UMP LIGHT

I SOLATED DC BUS ON BATTERY LIGHT

V OLTMETER DC

E MERGENCY DEPRESSURIZATION

E MERGENCY EXIT LIGHTS EXTINGUISH

E LT

S KE BATTERY

Busses located behind respective Circuit Breaker panel

Aft Junction box contains Circuit Breaker for flap and trim indicators

ELECTRICAL SYSTEM MALFUNCTIONS

Electrical Fire

Smoke and Fume elimination check list

Locate source and Isolate bus or specific device

Generator Out (Lite) - Check it out VOLTS/FREQS/LOAD

Lite illuminates for:

FREQ< 368 Hz

VOLT< 70 V on any phase

VOLT> 131-135 volts, field trip will be activated

For Confirmed Gen out on ground;  Place engine in Ground Stop

If Load, Volts and Freq check; leave Gen on and monitor

If No load but all else is ok; Contactor failure, Gen OFF Monitor

If Freq, Volt and Load 0:	Gen  RESET OFF

If Gen does not does not reset or has failed

GOUND STOP on ground

Disconnect Gen or ENG SHUT DOWN in flight

BUS OFF (Lite) - Turn it off (generator powering that bus)

Lite will come on for average phase voltage < 90 V

AC BUS OFF - Turn off the affected gen. Insure other gen pick up load

Check systems on bus for failure and freq volts load

If not ok leave gen off or for no indication; gen disconnect procedure.

ISOL DC ON BAT - confirm by checking BAT voltmeter.

If Volts <24 you have a problem, batt conservation required.

LOSS OF ESS AC (MGAIVER)

Indicated by:  loss Heading indication, aux pump failure, No2 Fuel boost pump flicker, loss of prop synchrophaser,  suction hydraulic boost pumps, auto pilot, normal brakes

M ech gov on prop

G en for that bus off (usually #2)

A nalyze (if ESS AC restored gen off, props to normal)

ELSE

A nti - Skid off

I nverters on CP and AC inst bus to DC pwr

V VG on vertical gyro

E Ess AC Check

R educe load fast

CP Instrument bus

Powered by either ESS AC or Isolated DC via inverter

FUEL SYSTEM

8 TANKS

No1 Main / No2 Main / LH Ext / LH Aux/ =/ RH Aux / RH Ext / No3 Main / No4 Main

TANK PUMP LIMITS

Main tanks

Pump Press   : 15-24 psi

Low press lite: