LL-1 (N4401): 9/4/05

·	Low-Level Brief

* As Required

·	JOG/TPC Charts

* [FTI]  Use a TPC for the route, use a JOG for the DZ run-in.  Make sure all crewmembers are using the same scale.

[Class Gouge] TPC 1:500,000; Updated less often, CHUM is more current.  JOG 1:250,000, updated more often, not as much CHUM.  Obviously smaller scale less area, more detail.

·	CHUM

* [FTI]  The CHUM has a cumulative listing of all obstacles 200 ft or higher.  In multiple complex, only highest one is listed.  Plot all CHUM w/I 22 NM of course centerline.

Can use CHUM manual, eCHUM or the CHUM off of FalconView.  Annotate the date of the CHUM used.

[Class Gouge] eCHUM might not include powerlines.  Use the symbology provided.

·	Student Chart Critique

* As Required

·	Copilot Airdrop Duties

* [FTI]

Slowdown:  Drop altitude = highest LZ altitude + 1000 ft.  Slowdown should be planned to stabilize on airspeed and altitude 1 min prior to TOT.  During day, climb required (500 AGL->1000 AGL.)  Call "thirty sec to slowdown, five seconds to slowdown, slowdown, slowdown, now."  PAC power idle, 1000 fpm climb.  On speed, flaps approach.  Slow to 120 KIAS.  During Night, same, but stay level.  When DZ in sight and will remain in sight, or a positive solution established and terrain clearance ensured, can descend to DZ alt.  No timing adjustments from slowdown to DZ.

Airdrop:  DZ appearance prebriefed, one minute prior to PI (point of impact) call "one minute advisory"  5 sec prior, call "five seconds." When over the DZ, call "green light."  Green light time is usable drop time.  When load clear, call 'load clear' 'Red light' will be called at the expiration of green light time.  We have simulated 7 sec of green light time.